This file describes the loading process of Linux used by BOOTLIN.
People not interested in modifying the assembler source of BootLinux
should not read this document (except those that are curious).

Here are the steps of loading process:
(1)	clear screen, print system configuration and check for
	386, 640K base memory and 1M extended memory.
	shrink the stack to lower the lowest address usable for loading
	the kernel.
(2)	parse options
(3)	try to open the image file. possibly ask a new name and retry(3).
(4)	load bootsector at 9000h:0; check for AA55h bootable flag at 9000h:1FEh
(5)	determine setup length, using the sector count found at offset 497 in
	the boot sector if present (or the default value of 4); load setup at
	9020h:0
(6)	loads the kernel into memory. Two strategies are possible, depending
	on BOOTLIN loading address in the base memory:
0      1      2      3      4      5      6      7      8      9      A x 64K
|------|------|------|------|------|------|------|------|------|------
<-(a)->								^-(c)
       <--------------------------(b)------------------------->
								 (d)-^
	(c) is the loading zone of bootsector and setup. (length 8K)
	(d) is reserved for moving some part of BOOTLIN. (length 4K)
	BOOTLIN is approx. 6K, so the total reserved memory is 18K, and a
	kernel will be loadable if its size remains less than <free mem> - 18K.

(6a)	BOOTLIN is loaded in (a): the kernel is directly loaded in the
	part of memory it expects to be. If the kernel is more than 512K,
	the remaining part will be loaded between (c) and (d), then an
	error message will be issued (kernel more than 512K or not enough
	memory).

(6b)	BOOTLIN extends over (b) (this is mainly the case if BootLinux is run
	from the DOS command line): the kernel is loaded just after the stack
	of BOOTLIN, up to the end of (b). If more of the image is to be loaded,
	it is loaded between (c) and (d). If more is to be loaded, then there
	is not enough memory, and the corresponding message is issued.
	The space between (c) and (d) is 64-4-8=52K.

(7)	the bootsector is updated with informations provided on the command
	line via options, and the informations about LINUX are displayed.

(8)	checks for non-null root fs device number. If this is not the case,
	asks for it and redisplay LINUX informations.

(9)	run LINUX, depending on wether (6) was (6a) or (6b):

(6a)->(9a)	BOOTLIN redirects Int 15h (in case HIMEM.SYS is loaded), then
	merely jumps into the setup code.

(6b)->(9b)	the setup does a few things, then finally jumps into
	the kernel code, expecting it at address 1000h:0. This is
	obviously not the case here.
	The kernel code could be moved to its right address before
	jumping to the setup, but it would crash DOS programs and DOS
	itself, so it is not possible because the setup uses a few
	DOS/BIOS interrupts: int 11h, 13h, 15h and 16h. Int 13h may be
	redirected by a disk cache, and Int 15h is nearly always redirected
	by HIMEM.SYS.
	The solution is to wait the call to the last interrupt to move
	the kernel code to its right place. After the move, interrupts must
	be disabled (cli) to avoid a possible call to Int 8 (timer) that would
	crash the computer.
	This is done by moving the appropriate BOOTLIN move code in zone
	(d), and redirecting int 13h and int 15h to this code.
	To handle correctly linux v1.1, int 11h is also redirected and
	emulated; it is actually the last int called, but this way int 13h
	can still be considered the last, and the one that must do the hard
	job.
	In fact, it is int 13h that can be considered called the last, but
	int 15h has to be redirected in every case, since the possible presence
	of HIMEM.SYS would make Int 15h report a false value of the
	available extended memory. The real value is always fetched by
	BOOTLIN in the CMOS, for its own use first, then to supply to
	the setup when it needs it.
	Linux 1.1's setup also calls int 13h twice with the same parameters,
	the first being a dummy one ("Bootlin needs this to be done early" !).
	Some code has added to check that int 13h will do its job only if the
	int 15h has already been called.

NOTE that (9b) operations depend closely on the setup calling given
interrupts in a given order with given parameters in the registers.
A change of these dependencies in the setup would imply:
(1) changes in BootLinux, possibly major.
(2) nearly sure incompatibility with previous versions.

NOTE the setup changed in linux v1.1, but BootLinux could be adapted to it
and remains compatible with previous versions.